## Slide 1
IT5002
Computer Systems and Applications
Datapath Design
colintan@nus.edu.sg

## Slide 2: Q & A
Please ask questions at https://piazza.com/class/me6eor4hpe0374
OR scan this QR code (may be obscured on some slides)

## Slide 3: Lecture #7: Datapath Design
Building a Processor: Datapath & Control
MIPS Processor: Implementation
Instruction Execution Cycle (Recap)
MIPS Instruction Execution
Let’s Build a MIPS Processor
  5.1 Fetch Stage
  5.2 Decode Stage
  5.3 ALU Stage
  5.4 Memory Stage
  5.5 Register Write Stage
The Complete Datapath!

## Slide 4
1. Building a Processor: Datapath & Control
Two major components for a processor
Datapath
Collection of components that process data
Control
Tells the datapath, memory and I/O devices what to do according to program instructions
Performs the arithmetic, logical and memory operations

## Slide 5
2. MIPS Processor: Implementation
Simplest possible implementation of a subset of the core MIPS ISA:
  Arithmetic and Logical operations
    add, sub, and, or, addi, andi, ori, slt
  Data transfer instructions
    lw, sw
  Branches
    beq, bne
Shift instructions (sll, srl) and J-type instructions (j) will not be discussed:
  Left as exercises 

## Slide 6
3. Instruction Execution Cycle (Basic)
Fetch:
  Get instruction from memory
  Address is in Program Counter (PC) Register
Decode:
  Find out the operation required
Operand Fetch:
  Get operand(s) needed for operation
Execute:
  Perform the required operation
Result Write (Store):
  Store the result of the operation
Instruction
Fetch
Instruction
Decode
Operand
Fetch
Execute
Result
Write
Next Instruction

## Slide 7
4. MIPS Instruction Execution (1/2)
Show the actual steps for 3 representative MIPS instructions
Fetch and Decode stages not shown:
  The standard steps are performed
 | add $3, $1, $2 | lw $3, 20( $1 ) | beq $1, $2, label
Fetch | standard | standard | standard
Decode |  |  | 
Operand Fetch | Read [$1] as opr1 Read [$2] as opr2 | Read [$1] as opr1 Use 20 as opr2 | Read [$1] as opr1 Read [$2] as opr2
Execute | Result = opr1 + opr2 | MemAddr = opr1 + opr2 Use MemAddr to read from memory | Taken = (opr1 == opr2 )? Target = (PC+4) + ofst4
Result Write | Result stored in $3 | Memory data stored in $3 | if (Taken) PC = Target
opr = operand
MemAddr = Memory Address
ofst = offset
add $3, $1, $2
lw $3, 20($1)
beq $1, $2, ofst

## Slide 8
4. MIPS Instruction Execution (2/2)
Design changes:
  Merge Decode and Operand Fetch – Decode is simple for MIPS
  Split Execute into ALU (Calculation) and Memory Access
 | add $3, $1, $2 | lw $3, 20( $1 ) | beq $1, $2, label
Fetch | Read inst. at [PC] | Read inst. at [PC] | Read inst. at [PC]
Decode & Operand Fetch | Read [$1] as opr1 Read [$2] as opr2 | Read [$1] as opr1 Use 20 as opr2 | Read [$1] as opr1 Read [$2] as opr2
ALU | Result = opr1 + opr2 | MemAddr = opr1 + opr2 | Taken = (opr1 == opr2 )? Target = (PC+4) + ofst4
Memory Access |  | Use MemAddr to read from memory | 
Result Write | Result stored in $3 | Memory data stored in $3 | if (Taken) PC = Target
add $3, $1, $2
lw $3, 20($1)
beq $1, $2, ofst

## Slide 9
5. Let’s Build a MIPS Processor
What we are going to do:
  Look at each stage closely, figure out the requirements and processes
  Sketch a high level block diagram, then zoom in for each elements
  With the simple starting design, check whether different type of instructions can be handled:
    Add modifications when needed
 Study the design from the viewpoint of a designer, instead of a "tourist" 

## Slide 10
5.1 Fetch Stage: Requirements
Instruction Fetch Stage:
  Use the Program Counter (PC) to fetch the instruction from memory
    PC is implemented as a special register in the processor
  Increment the PC by 4 to get the address of the next instruction:
    How do we know the next instruction is at PC+4?
    Note the exception when branch/jump instruction is executed
Output to the next stage (Decode):
  The instruction to be executed
Fetch
Decode
ALU
Memory
RegWrite

## Slide 11
5.1 Fetch Stage: Block Diagram
Add
PC
4
Read
address
Instruction
Instruction
memory
A register
Memory which stores program instructions
A simple adder
Decode Stage
Instruction

## Slide 12
5.1 Element: Instruction Memory
Storage element for the instructions
  It is a sequential circuit (to be covered later)
  Has an internal state that stores information
  Clock signal is assumed and not shown
Supply instruction given the address
  Given instruction address M as input, the memory outputs the content at address M
  Conceptual diagram of the memory layout is given on the right 
Instruction
Memory
Instruction
Address
Instruction
Memory
2048
2052
2056
andi $1, $4, 0xF
sll $4, $3, 2
add $3, $1, $2
……
………..
………..

## Slide 13
5.1 Element: Adder
Combinational logic to implement the addition of two numbers
Inputs:
  Two 32-bit numbers A, B
Output:
  Sum of the input numbers, A + B
A
B
A+B
Sum
Add
32
32
32

## Slide 14
5.1 The Idea of Clocking
It seems that we are reading and updating the PC at the same time:
  How can it works properly?
Magic of clock:
  PC is read during the first half of the clock period and it is updated with PC+4 at the next rising clock edge
Add
PC
4
Read
address
Instruction
Instruction
memory
In
Clk
Time
PC
100
104
108
112
In
104
108
112
116

## Slide 15
5.2 Decode Stage: Requirements
Instruction Decode Stage:
  Gather data from the instruction fields:
  Read the opcode to determine instruction type and field lengths
  Read data from all necessary registers
    Can be two (e.g. add), one (e.g. addi) or zero (e.g. j)
Input from previous stage (Fetch):
  Instruction to be executed
Output to the next stage (ALU):
  Operation and the necessary operands
Fetch
Decode
ALU
Memory
RegWrite

## Slide 16
5.2 Decode Stage: Block Diagram
Fetch Stage
Inst.
Data
Register
numbers
ALU Stage
Operands
Collection of registers, known as register file
Read
register 1
Read
register 2
Write
register
Read
data 1
Read
data 2
Register
File
5
5
5
32
32

## Slide 17
5.2 Element: Register File
A collection of 32 registers:
  Each 32-bit wide; can be read/written by specifying register number
  Read at most two registers per instruction
  Write at most one register per instruction
RegWrite is a control signal to indicate:
  Writing of register
  1(True) = Write, 0 (False) = No Write
32
Read
register 1
Read
register 2
Write
register
Write
data
Read
data 1
Read
data 2
RegWrite
Data
Data
Register
numbers
Register
File
5
5
5
32
32

## Slide 18
5.2 Decode Stage: R-Format Instruction
opcode
31:26
rs
25:21
rt
20:16
rd
15:11
shamt
10:6
funct
5:0
000000
01001
01010
01000
00000
100000
content of register $9
content of register $10
Result to be stored into register $8 (produced by later stage)
Inst [25:21]
Inst [20:16]
Inst [15:11]
Notation:
Inst [Y:X]
= bits X to Y in Instruction
add $8, $9, $10
RegWrite
Read
register 1
Read
register 2
Write
register
Write
data
Read
data 1
Read
data 2
Register
File
5
5
5
32
32
32

## Slide 19
5.2 Decode Stage: I-Format Instruction
content of register $22
001000
10110
10101
1111 1111 1100 1110
Immediate
15:0
opcode
31:26
rs
25:21
rt
20:16
Inst [25:21]
Inst [20:16]
Inst [15:11]
addi $21, $22, -50
Problems:
Destination $21 is in the "wrong position"
Read Data 2 is an immediate value, not from register
Read
register 1
Read
register 2
Write
register
Write
data
Read
data 1
Read
data 2
RegWrite
Register
File
5
5
5
32
32

## Slide 20
5.2 Decode Stage: Choice in Destination
001000
10110
10101
1111 1111 1100 1110
Immediate
15:0
opcode
31:26
rs
25:21
rt
20:16
Inst [25:21]
addi $21, $22, -50
Read
register 1
Read
register 2
Write
register
Write
data
Read
data 1
Read
data 2
RegWrite
Register
File
5
5
5
32
32
RegDst:
A control signal to choose either Inst[20:16] or Inst[15:11] as the write register number
Solution (Write Reg. No.):
Use a multiplexer to choose the correct write register number based on instruction type
Inst [20:16]
Inst [15:11]
MUX
RegDst
content of register $22

## Slide 21
5.2 Multiplexer
Function:
  Selects one input from multiple input lines
Inputs:
  n lines of same width
Control:
  m bits where n = 2m
Output:
  Select ith input line if control = i
Control=0  select in0 to out
Control=3  select in3 to out
in0
inn-1
out
control
m
.
.
.
MUX

## Slide 22
5.2 Decode Stage: Choice in Data 2
001000
10110
10101
1111 1111 1100 1110
Immediate
15:0
opcode
31:26
rs
25:21
rt
20:16
Inst [25:21]
addi $21, $22, -50
Read
register 1
Read
register 2
Write
register
Write
data
Read
data 1
Read
data 2
RegWrite
Register
File
5
5
5
32
32
Inst [20:16]
Inst [15:11]
MUX
RegDst
ALUSrc:
A control signal to choose either "Read data 2" or the sign extended Inst[15:0] as the second operand
Solution (Rd. Data 2):
Use a multiplexer to choose the correct operand 2.
Sign extend the 16-bit immediate value to 32-bit
Inst [15:0]
MUX
ALUSrc
Sign Extend
16
32
content of register $22

## Slide 23
5.2 Decode Stage: Load Word Instruction
100011
10110
10101
1111 1111 1100 1110
Immediate
15:0
opcode
31:26
rs
25:21
rt
20:16
Inst [25:21]
lw $21, -50($22)
Read
register 1
Read
register 2
Write
register
Write
data
Read
data 1
Read
data 2
RegWrite
Register
File
5
5
5
32
32
Inst [20:16]
Inst [15:11]
MUX
RegDst
Inst [15:0]
MUX
ALUSrc
Sign Extend
16
32
content of register $22
Do we need any modification?

## Slide 24
5.2 Decode Stage: Branch Instruction
000100
01001
00000
0000 0000 0000 0011
Immediate
15:0
opcode
31:26
rs
25:21
rt
20:16
Inst [25:21]
beq $9, $0, 3
Read
register 1
Read
register 2
Write
register
Write
data
Read
data 1
Read
data 2
RegWrite
Register
File
5
5
5
32
32
Inst [20:16]
Inst [15:11]
MUX
RegDst
Inst [15:0]
MUX
ALUSrc
Sign Extend
16
32
content of register $9
Need to calculate branch outcome and target at the same time!
We will tackle this problem at the ALU stage

## Slide 25
5.2 Decode Stage: Summary
Read
register 1
Read
register 2
Write
register
Write
data
Read
data 1
Read
data 2
Register
File
5
5
5
Inst [25:21]
Inst [20:16]
Inst [15:11]
MUX
RegDst
Inst [15:0]
MUX
ALUSrc
RegWrite
Sign Extend
16
32
Operand 1
Operand 2
Inst[31:0]
32
32

## Slide 26
5.3 ALU Stage: Requirements
Instruction ALU Stage:
  ALU = Arithmetic-Logic Unit
  Also called the Execution stage
  Perform the real work for most instructions here
    Arithmetic (e.g. add, sub), Shifting (e.g. sll), Logical (e.g. and, or)
    Memory operation (e.g. lw, sw): Address calculation
    Branch operation (e.g. bne, beq): Perform register comparison and target address calculation
Input from previous stage (Decode):
  Operation and Operand(s)
Output to the next stage (Memory):
  Calculation result
Fetch
Decode
ALU
Memory
RegWrite

## Slide 27
Logic to perform arithmetic and logical operations
5.3 ALU Stage: Block Diagram
ALU result
ALU
Decode Stage
Operands
Memory Stage

## Slide 28
5.3 Element: Arithmetic Logic Unit
ALU (Arithmetic Logic Unit)
  Combinational logic to implement arithmetic and logical operations
Inputs:
  Two 32-bit numbers
Control:
  4-bit to decide the particular operation
Outputs:
  Result of arithmetic/logical operation
  A 1-bit signal to indicate whether result is zero
ALUcontrol | Function
0000 | AND
0001 | OR
0010 | add
0110 | subtract
0111 | slt
1100 | NOR
ALU
result
ALU
ALUcontrol
4
isZero?
A
B
A op B
(A op B) == 0?
32
32
32

## Slide 29
5.3 ALU Stage: Non-Branch Instructions
We can handle non-branch instructions easily:
add $8, $9, $10
Read
register 1
Read
register 2
Write
register
Write
data
Read
data 1
Read
data 2
Register
File
5
5
5
Inst [25:21]
Inst [20:16]
Inst [15:11]
MUX
RegDst
Inst [15:0]
MUX
ALUSrc
RegWrite
Sign Extend
16
32
ALU
result
ALU
ALUcontrol
4
isZero?
opcode
31:26
rs
25:21
rt
20:16
rd
15:11
shamt
10:6
funct
5:0
000000
01001
01010
01000
00000
100000
32
32
32
ALUcontrol:
Set using opcode + funct field (more in next lecture)

## Slide 30
5.3 ALU Stage: Branch Instructions
Branch instruction is harder as we need to perform two calculations:
Example: "beq $9, $0, 3"
  Branch Outcome:
    Use ALU to compare the register
    The 1-bit "isZero?" signal is enough to handle equal/not equal check (how?)
  Branch Target Address:
    Introduce additional logic to calculate the address
    Need PC (from Fetch Stage)
    Need Offset (from Decode Stage)

## Slide 31
000100
01001
00000
0000 0000 0000 0011
Immediate
15:0
opcode
31:26
rs
25:21
rt
20:16
Read
register 1
Read
register 2
Write
register
Write
data
Read
data 1
Read
data 2
Register
File
5
5
5
Inst [25:21]
Inst [20:16]
Inst [15:11]
MUX
RegDst
Inst [15:0]
MUX
ALUSrc
RegWrite
Sign Extend
16
32
ALU
result
ALU
ALUcontrol
4
isZero?
Left Shift 2-bit
PC
Add
4
Add
MUX
PCSrc
Complete ALU Stage
PCSrc:
Control Signal to select between (PC+4) or Branch Target
beq $9, $0, 3
32
32
32

## Slide 32
5.4 Memory Stage: Requirements
Instruction Memory Access Stage:
  Only the load and store instructions need to perform operation in this stage:
    Use memory address calculated by ALU Stage
    Read from or write to data memory
  All other instructions remain idle
    Result from ALU Stage will pass through to be used in Register Write stage (see section 5.5) if applicable
Input from previous stage (ALU):
  Computation result to be used as memory address (if applicable)
Output to the next stage (Register Write):
  Result to be stored (if applicable)
Fetch
Decode
ALU
Memory
RegWrite

## Slide 33
5.4 Memory Stage: Block Diagram
Memory which stores data values
ALU Stage
Result
Register Write Stage
Data
Memory
Address
Read
Data
Write
Data
MemRead
MemWrite
32
32
32

## Slide 34
5.4 Element: Data Memory
Storage element for the data of a program
Inputs:
  Memory Address
  Data to be written (Write Data) for store instructions
Control:
  Read and Write controls; only one can be asserted at any point of time
Output:
  Data read from memory (Read Data) for load instructions
Data
Memory
Address
Read
Data
Write
Data
MemRead
MemWrite
32
32
32

## Slide 35
5.4 Memory Stage: Load Instruction
Only relevant parts of Decode and ALU Stages are shown
lw $21, -50($22)
000100
01001
00000
0000 0000 0000 0011
Immediate
15:0
opcode
31:26
rs
25:21
rt
20:16
Inst [25:21]
Inst [20:16]
Inst [15:11]
MUX
RegDst
Inst [15:0]
MUX
ALUSrc
RR1
RR2
WR
WD
RD1
RD2
Register
File
5
5
5
RegWrite
Sign Extend
16
32
ALU
result
ALU
ALUcontrol
4
100011
10110
10101
1111 1111 1100 1110
Address
Write
Data
MemRead
MemWrite
Data
Memory
Read
Data
32
32
32
32

## Slide 36
5.4 Memory Stage: Store Instruction
Need Read Data 2 (from Decode stage) as the Write Data
sw $21, -50($22)
000100
01001
00000
0000 0000 0000 0011
Immediate
15:0
opcode
31:26
rs
25:21
rt
20:16
Inst [25:21]
Inst [20:16]
Inst [15:11]
MUX
RegDst
Inst [15:0]
MUX
RR1
RR2
WR
WD
RD1
RD2
Register
File
5
5
5
RegWrite
Sign Extend
16
32
ALU
result
ALU
ALUcontrol
4
101011
10110
10101
1111 1111 1100 1110
Address
Write
Data
MemRead
MemWrite
Data
Memory
Read
Data
32
32
32
32

## Slide 37
5.4 Memory Stage: Non-Memory Inst.
Add a multiplexer to choose the result to be stored
add $8, $9, $10
Inst [25:21]
Inst [20:16]
Inst [15:11]
MUX
RegDst
Inst [15:0]
MUX
RR1
RR2
WR
WD
RD1
RD2
Register
File
5
5
5
RegWrite
Sign Extend
16
32
ALU
result
ALU
ALUcontrol
4
Data
Memory
Address
Read
Data
Write
Data
MemWrite
opcode
31:26
rs
25:21
rt
20:16
rd
15:11
shamt
10:6
funct
5:0
000000
01001
01010
01000
00000
100000
MUX
MemToReg
32
32
MemToReg:
A control signal to indicate whether result came from memory or ALU unit

## Slide 38
5.5 Register Write Stage: Requirements
Fetch
Decode
ALU
Memory
RegWrite
Instruction Register Write Stage:
  Most instructions write the result of some computation into a register
    Examples: arithmetic, logical, shifts, loads, set-less-than
    Need destination register number and computation result
  Exceptions are stores, branches, jumps:
    There are no results to be written
    These instructions remain idle in this stage
Input from previous stage (Memory):
  Computation result either from memory or ALU

## Slide 39
5.5 Register Write Stage: Block Diagram
Result Write stage has no additional element:
  Basically just route the correct result into register file
  The Write Register number is generated way back in the Decode Stage
Memory Stage
Result
Read
register 1
Read
register 2
Write
register
Read
data 1
Read
data 2
Register
File
5
5
5
Write
data

## Slide 40
5.5 Register Write Stage: Routing
Inst [25:21]
Inst [20:16]
Inst [15:11]
MUX
Inst [15:0]
MUX
RR1
RR2
WR
WD
RD1
RD2
Register
File
5
5
5
RegWrite
Sign Extend
ALU
result
ALU
ALUcontrol
4
Data
Memory
Address
Read
Data
Write
Data
MemWrite
opcode
31:26
rs
25:21
rt
20:16
rd
15:11
shamt
10:6
funct
5:0
000000
01001
01010
01000
00000
100000
MUX
MemToReg
add $8, $9, $10

## Slide 41
6. The Complete Datapath!
We have just finished “designing” the datapath for a subset of MIPS instructions:
  Shifting and Jump are not supported
Check your understanding:
  Take the complete datapath and play the role of controller:
    See how supported instructions are executed
    Figure out the correct control signals for the datapath elements
Coming up next: Control

## Slide 43
Complete Datapath
Inst [25:21]
Inst [20:16]
Inst [15:11]
MUX
Inst [15:0]
MUX
RR1
RR2
WR
WD
RD1
RD2
Register
File
5
5
5
RegWrite
Sign Extend
ALU
result
ALU
ALUcontrol
4
Data
Memory
Address
Read
Data
Write
Data
MemWrite
opcode
31:26
rs
25:21
rt
20:16
rd
15:11
shamt
10:6
funct
5:0
000000
01001
01010
01000
00000
100000
Left Shift 2-bit
PC
Add
4
Add
MUX
PCSrc
Instruction
Memory
is0?
Address
Instruction
RegDst
MemRead
ALUSrc
MemToReg
MUX